## Slide 1
SOS
EMERGENCY BEACON
433 MHz · ESP32 · LoRa · FreeRTOS
Department of Electronics & Communication
2026
OFFLINE
ESP32 LoRa Mesh
SOS Emergency Communication System
Captive Portal
Mesh Relay
Rescue Dashboard
~3 km
< $15
0 Internet
LoRa Range
Cost / Node
Required
Offline ESP32 LoRa Mesh SOS System · Full Firmware + Captive Portal + Rescue Dashboard
1 / 11

## Slide 2
Table of Contents
What we will cover today
01
Project Overview & Motivation
Why offline LoRa beats cellular in emergencies
02
System Architecture
3-node mesh: Transmitter → Relay → Base Station
03
Hardware & Wiring
ESP32 + LoRa SX1278 + I²C LCD pin mapping
04
Node 1 — SOS Transmitter
Captive Portal + PWA + RTOS dual-core LoRa task
05
Node 2 — Base Station
LCD alarms + Rescue Dashboard + ACK broadcast
06
Node 3 — Mesh Relay
Hop limit, dedup cache, jitter anti-collision
07
Software Stack
Arduino IDE, libraries, FreeRTOS architecture
08
Live Demo Flow
8-step walkthrough: Power Up → SAVED
09
Technical Deep-Dive
Thread safety, reliability, captive portal compat
10
Results & Future Work
Achievements, cost summary, enhancements roadmap
Offline ESP32 LoRa Mesh SOS System
2 / 11

## Slide 3
01 — Project Overview & Motivation
Disaster scenarios where cellular networks fail but LoRa still works
THE PROBLEM
Earthquakes, floods & tsunamis destroy cell towers first
GPS satellites still function — but data has nowhere to go
Victims cannot call for help or share their location
Rescue teams operate blind without victim coordinates
Satellite communicators (Garmin inReach) cost $400–$600
GSM modules require SIM cards, data plans & signal coverage
OUR SOLUTION
Self-contained mesh using ESP32 + LoRa — no infrastructure
Victim's phone connects to WiFi hotspot (no SIM needed)
Browser auto-opens SOS web app via Captive Portal
GPS coords transmitted over LoRa radio to rescue base
Rescue team views real-time dashboard, resolves & ACKs
Total hardware cost: under $15 per node (~₹1,200)
Offline ESP32 LoRa Mesh SOS System
3 / 11

## Slide 4
02 — System Architecture
End-to-end packet flow: victim phone → LoRa mesh → rescue operator
NODE 1
SOS TRANSMITTER
WiFi AP: SOS_EMERGENCY_AP
IP: 192.168.4.1
Captive Portal Web App
RTOS LoRa TX (Core 0)
NODE 3
MESH RELAY
WiFi AP: RELAY_NODE_3
IP: 192.168.6.1
Hop limit: 2
Jitter: 50–180 ms
NODE 2
BASE STATION
WiFi AP: RESCUE_BASE_AP
IP: 192.168.5.1
I²C LCD Display
Rescue Dashboard
SOS ▶
◀ ACK
SOS ▶
◀ ACK
PACKET FORMATS
SOS: "SOS:[ID]:[LAT]:[LON]:[HOPS]" e.g. SOS:1749382:12.9716:77.5946:1
ACK: "ACK:[ID]:[HOPS]" e.g. ACK:1749382:1
LoRa 433 MHz · SF7 · BW 125kHz · CR 4/5
Offline ESP32 LoRa Mesh SOS System
4 / 11

## Slide 5
03 — Hardware Components & Wiring
SPI pin mapping identical across all three nodes — 3.3 V strict
BILL OF MATERIALS
Component
Used on
Cost
ESP32 WROOM-32
All nodes
~$4.00
LoRa SX1278 (Ra-02)
All nodes
~$4.50
16×2 I²C LCD
Node 2 only
~$2.50
Jumper wires
All nodes
~$1.00
USB cable
Programming
~$1.00
Breadboard
Prototyping
~$1.50
SPI WIRING — ALL NODES
LoRa Pin
ESP32 GPIO
Function
VCC
3.3 V
Power — NEVER connect to 5V!
GND
GND
Ground
MISO
GPIO 19
SPI Master In Slave Out
MOSI
GPIO 23
SPI Master Out Slave In
SCK
GPIO 18
SPI Clock
NSS
GPIO 5
SPI Chip Select
RST
GPIO 14
Module Reset
DIO0
GPIO 4
Interrupt (not GPIO 2)
⚠ CRITICAL: LoRa SX1278 / Ra-02 operates at 3.3 V strictly. Applying 5 V to VCC will permanently destroy the RF front-end.
Offline ESP32 LoRa Mesh SOS System
5 / 11

## Slide 6
04 — Node 1: SOS Transmitter
WiFi Captive Portal + Embedded PWA + RTOS LoRa broadcast
CAPTIVE PORTAL
SSID: SOS_EMERGENCY_AP (open — no password)
DNS wildcard: any domain → 192.168.4.1
Android support: /generate_204 endpoint
Windows support: /fwlink endpoint
HTML/CSS/JS embedded in ESP32 flash (app_html.h)
SOS WEB APP (PWA)
Auto-reads GPS via browser Geolocation API
Manual coordinate entry if GPS is denied
Glowing SOS button — tap to broadcast
Polls /status every 2 s: IDLE → BROADCASTING → SAVED
Installable as offline PWA (manifest.json + sw.js)
RTOS DUAL-CORE ARCHITECTURE
CORE 0 — loraTask()
• Retransmits SOS every 4 s (or on new packet ID)
• Listens for incoming ACK packets
• Auto-timeout: 60 s with no ACK → resets to IDLE
CORE 1 — Web Server + DNS Loop
• Handles HTTP: /send_sos, /status, /reset_status
• dnsServer.processNextRequest() — captive portal
• RTOS mutex (loraMutex) guards all SPI access
mutex
Offline ESP32 LoRa Mesh SOS System
6 / 11

## Slide 7
05 — Node 2: Base Station Receiver
LCD alarm + Rescue Dashboard + non-blocking ACK broadcast on Core 0
LORA RECEPTION & LCD
Parses SOS:[ID]:[LAT]:[LON]:[HOPS] — strips hop field
Stores up to 10 alerts in memory (struct SOSAlert[])
De-duplicates by packet ID — silent re-RSSI update
LCD row 0: "SOS! RSSI:−72dB" | Row 1: coordinates
Backlight flashes at 200 ms for 1 s to attract attention
RESCUE DASHBOARD (http://rescue.local)
WiFi AP: RESCUE_BASE_AP | IP: 192.168.5.1
mDNS: http://rescue.local (ESPmDNS library)
Live alert list: ID, RSSI, coords, Google Maps link
"Resolve" → spawns RTOS ackSendTask on Core 0
LCD shows "RESCUED! ACK Sent" with coordinates
ACK BROADCAST SEQUENCE (Core 0 — non-blocking)
1
Operator
clicks Resolve
2
alert.active
= false
3
malloc(AckJob)
struct on heap
4
xTaskCreatePinnedToCore
Core 0 ackSendTask
5
Send ACK 3×
400 ms gaps
6
free(job)
vTaskDelete
Offline ESP32 LoRa Mesh SOS System
7 / 11

## Slide 8
06 — Node 3: Mesh Relay / Repeater
Hop-limited, dedup-cached, jitter-delayed intelligent relay node
RELAY LOGIC
Listens on 433 MHz for SOS and ACK packets
Hop-limit check: discard if HOPS ≥ 2 (configurable)
Seen-cache ring buffer (30 entries) blocks duplicates
Increments hop count, rebuilds packet before relay
Schedules relay after random jitter (50–180 ms)
GPIO 2 LED blinks 30 ms on each forwarded packet
RELAY STATUS DASHBOARD (192.168.6.1)
WiFi AP: RELAY_NODE_3 (no DNS, direct IP access)
Shows last 12 relayed events with RSSI + timestamp
Live counters: SOS forwarded / ACK forwarded / Drops
JSON API: GET /status_json (poll from any client)
Malformed packet detection with serial debug output
WHY RANDOM JITTER?
If Node 1 (just transmitted) and Node 3 (about to relay) both transmit simultaneously, the signals collide on 433 MHz and corrupt each other — neither packet is received correctly.
Random jitter staggers TX windows. Same principle as CSMA/CA in WiFi and Bluetooth FHSS.
Offline ESP32 LoRa Mesh SOS System
8 / 11

## Slide 9
07 — Software Stack & Libraries
Arduino IDE + ESP32 board package + FreeRTOS — all open-source, free
Library
Author
Key APIs Used in this Project
LoRa
Sandeep Mistry
SPI LoRa driver — beginPacket / endPacket / parsePacket / packetRssi
LiquidCrystal_I2C
F. de Brabander
I²C 16×2 LCD — init, backlight, noBacklight, print, setCursor
WiFi.h
ESP32 built-in
WIFI_AP_STA mode — softAP, softAPConfig, begin, SSID, localIP
WebServer.h
ESP32 built-in
HTTP server — on(), send(), sendHeader(), send_P(), method()
DNSServer.h
ESP32 built-in
DNS wildcard — start(port, "*", ip) for captive portal redirect
ESPmDNS.h
ESP32 built-in
Multicast DNS — MDNS.begin("rescue") → http://rescue.local
FreeRTOS
ESP-IDF / built-in
xTaskCreatePinnedToCore, xSemaphoreCreateMutex, vTaskDelay, malloc
SETUP:
File › Preferences › add ESP32 board URL → Board Manager › "esp32 by Espressif" → Library Manager › LoRa + LiquidCrystal_I2C → Upload .ino to each node
Offline ESP32 LoRa Mesh SOS System
9 / 11

## Slide 10
08 — Live Demo: Step-by-Step Operation
Trace a complete SOS event from trigger to resolution
01
Power Up All Nodes
Connect all 3 ESP32s to USB power. Open Serial Monitor @ 115200 baud. Node 2 LCD shows "LoRa Ready / Waiting for data".
02
Connect to WiFi
On victim phone: Settings → WiFi → connect to "SOS_EMERGENCY_AP". No password required.
03
Captive Portal Opens
Phone auto-launches "SOS Emergency Beacon" in browser. GPS is silently read in background.
04
Trigger SOS
Tap the red SOS button. Status changes to BROADCASTING. ESP32 transmits LoRa every 4 seconds.
05
Node 3 Relays
Relay receives packet, checks seen-cache, increments hop count, waits jitter delay, re-broadcasts.
06
Node 2 Receives
LCD backlight flashes rapidly. Screen shows coordinates + RSSI. Dashboard auto-updates.
07
Operator Resolves
Operator connects to RESCUE_BASE_AP → opens http://rescue.local → clicks Resolve.
08
Victim Saved
ACK broadcast 3×. Node 3 relays ACK back. Node 1 receives → phone portal shows "SAVED ✅".
Offline ESP32 LoRa Mesh SOS System
10 / 11

## Slide 11
09 — Technical Deep-Dive
Thread safety, reliability patterns, captive portal compatibility
THREAD SAFETY
loraMutex (xSemaphoreCreateMutex) guards every LoRa SPI call
Core 0 task and Core 1 web handler never touch SPI simultaneously
AckJob allocated on heap — no shared String across cores
Volatile keyword on systemStatus for cross-core visibility
CAPTIVE PORTAL COMPAT.
/generate_204 → Android CNA (Captive Network Assist)
/fwlink → Windows Network Assessment Service
DNS wildcard (*) → all domains resolve to 192.168.4.1
Cache-Control: no-cache headers prevent stale portal page
RELIABILITY FEATURES
SOS retransmit every 4 s until ACK or 60 s hard timeout
ACK sent 3× with 400 ms spacing — survives single-packet loss
LoRa init failure handled gracefully (WiFi-only fallback)
RESOLVE:[ID] serial command bypasses WiFi if dashboard fails
DUPLICATE PREVENTION
Node 1: lastSentPacketID tracks in-flight packet ID
Node 2: addAlert() by ID — reactivates, never double-counts
Node 3: seenCache[30] ring buffer — O(n) scan before relay
Malformed packets detected and counted as drops silently
Offline ESP32 LoRa Mesh SOS System
11 / 11

## Slide 12
10 — Results & Future Work
Achievements, cost analysis, and the roadmap ahead
WHAT WE ACHIEVED
Complete offline SOS system — zero internet dependency
Captive portal with live GPS on any modern smartphone
Real-time Rescue Dashboard with Google Maps coordinates
Intelligent mesh relay — hop limit + collision avoidance
Thread-safe dual-core RTOS firmware architecture
Graceful degradation if LoRa hardware fails to init
FUTURE ENHANCEMENTS
Extend mesh with 5+ relay nodes (multi-hop routing)
AES-128 packet encryption to prevent SOS spoofing
Solar + LiPo power for 72-hour autonomous deployment
LoRaWAN uplink when internet is restored post-disaster
Multi-language portal (Hindi, Tamil, local languages)
Low-power deep sleep between transmit cycles
$4.00
ESP32 WROOM-32
$4.50
LoRa SX1278
$2.50
I²C LCD (Node 2)
$2.50
Wires & misc.
≈$13.50
Total / Node
Offline ESP32 LoRa Mesh SOS System
12 / 11

## Slide 13
THANK YOU
Questions & Discussion
Offline ESP32 LoRa Mesh SOS System
PROJECT SUMMARY
Node 1 → SOS_EMERGENCY_AP / 192.168.4.1
Node 2 → RESCUE_BASE_AP / http://rescue.local
Node 3 → RELAY_NODE_3 / 192.168.6.1
LoRa: 433 MHz | Baud: 115200 | Cost: < $15 / node
KEY SPECIFICATIONS
433 MHz
LoRa Frequency
~3 km
Open-air Range
2 Hops
Max Mesh Depth
< $15
Cost per Node
0
Internet Required
3
Total Nodes
Department of Electronics & Communication · 2026 · github.com/[your-handle]/lora-sos-mesh
13 / 11